## Slide 1: Grand Canal Greenway
Proposal for the information of the Members of the Clondalkin Area Committee
20 June 2018

## Slide 2: Grand Canal Greenway The proposed project will entail the following: • 4.6km of new 3.0m to 4m wide Shared Cycle & Pedestrian Greenway adjacent to the Grand Canal’s northern towpath from 12th Lock Bridge to Hazelhatch Bridge linking the existing Eastern Greenway to the Arthurs Way Greenway. • 0.45km of 4m wide Shared Cycle & Pedestrian Route connecting the proposed Grange Castle West Lands to the northern towpath of the Grand Canal including 150metres of elevated walkway overlooking a disused quarry. • Upgrade of the existing Gollierstown Bridge including pavement resurfacing and installation of additional fall protection. • 1 no. of new 4m wide Shared Cycle & Pedestrian Bridge located in the vicinity of Hazelhatch Bridge to provide connection with the existing Arthurs Way on the southern towpath. (This will form a future Part 8 application) • Greenway furniture including kissing gates, bollards, signage, markings and all associated safety features. • Street lighting and CCTV installations. • All associated landscape finishes and planting • 6500m new service way from 12th Lock to Aylmer Bridge located under the proposed Greenway. Services included will be Power (LV & HV) Communications (Telecom) CCTV Public Lighting • 1 no. of new service crossing under the Grand Canal adjacent to Gollierstown Bridge to connect the proposed Grand Canal service way to Grange Castle West Business Park.

## Slide 5
To Date:
At the May CPG, Council, Lucan Area Committee and Economic, Enterprise and Tourism Development SPC meetings briefings were given to the members on proposals for Greenway projects along the Grand Canal. eg
  Grand Canal / Royal Canal Loop
  Permeability the Arthurs Way
Waterways Ireland have requested that Dublin City, South Dublin and Kildare County Councils prepare plans for the Greenway. They have also indicated that they would like to commence the scheme next year.
The Grand Canal in South Dublin traverses the Kildare County Border before reaching Aylmer Bridge. In order to deliver the scheme at the earliest possible date the Council approved the entering into of a Section 85 agreement with Kildare County Council and the June Council Meeting
NTA have agreed to fund the design costs in the region of €142k plus Vat.

## Slide 6: Timeframe
Likely Part 8 approval of the members will be Sought in September 2018